## Slide 1: Digital Pizzabox – Overview
Functionality
  Motor positions capturing
  Detector triggering
  More with firmware customization
    Current resource utilization: registers 6%, LUTs 13%.
  Deployed at QAS, ISS, …
Encoders
Pizzabox
Turbo PMAC
Timing system
Detectors
Servers
Other triggering source

## Slide 2: Digital Pizzabox – What’s inside
NSLS-II BPM Digital Front End (DFE) board
  Virtex-6
  1GB DDR3 DRAM
Encoder interface board
Interfaces
  Quadrature incremental encoder
    Renishaw
    Delta Tau Turbo PMAC
  Timing system
    Timestamp (8 ns resolution)
    Triggering event
  Ethernet
  GPIO

## Slide 3: Digital Pizzabox – How it works

## Slide 4: Digital Pizzabox – How to communicate
EPICS soft IOC
Available PVs
  Encoder positions
  Device registers
  GPIO states

## Slide 5: Digital Pizzabox – How to interface
Record file – save, plot
Circular buffer status
Filtering parameter setup
Mode selection

## Slide 6: Digital Pizzabox – How well it performs
Circular buffer (DDR3 memory)
  256Mb per channel
  Data erased if buffer overflows
  Network
  LWIP
  Data rate in v.s. data rate out
Encoder signal processor
FIFO
Circular buffer (DDR3)
Network
NPI
800 Mb/S
NPI
800 Mb/S
1GBE
2 Mb/S

## Slide 7: Digital Pizzabox – Reference
FPGA project
Circuit (schematic/PCB) files
EPICS IOC
Ruslan Kadyrov, et el., Encoder Interface for NSLS-II Beam Line Motion Scanning Applications, ICALEPCS’15.